## Slide 1
OAI 5G NR Sidelink
Test Framework
Automated CI Test Harness for PC5 & U2N Relay Validation
PC5 Mode 1 & 2
CSI / PSFCH
U2N Relay (SRAP)
RF Sim, VRT Sim & USRP
OpenAirInterface — 2026

## Slide 2
Overview & Key Features
What It Tests
Sidelink Mode 2 — Direct D2D communication
Sidelink Mode 1 — Network-scheduled sidelink
U2N Relay (SRAP) — Remote UE connectivity via relay
CSI / PSFCH — Parametric feedback testing
Uu Interface — gNB <-> UE connectivity testing
iperf3 Bandwidth Sweep — UDP throughput characterization
BLER Testing — Waterfall curves across MCS 0-28 with noise sweep
Key Features
Array-based test selection — simple ordered list
Parametric sweeps — CSI x PSFCH combinations
Multi-host support — 1, 2, or 3 machines via SSH
Profile-based config — pilot / regress / stress / bler
Auto result tracking — ping + PSSCH statistics
Three radio backends — rfsim (socket) / usrp (B210 HW) / vrtsim (shared-memory, local host)
Two scripts: run_sl_test.sh (test engine) + run_sl_test_config.sh (user configuration)

## Slide 3
Architecture & Execution Flow
Execution Flow
1. Load config (run_sl_test_config.sh)
2. Resolve enabled_tests array
3. For each test:
a. Clean up old logs
b. Launch UEs (local / remote SSH)
c. Wait for tunnel interface
d. Wait for PC5 sync (PSBCH decode)
e. Execute ping test
f. Collect stats (ping + PSSCH)
g. Kill processes & cleanup
h. Generate summary row
4. Display final summary table
Duration budget (ensure_ping_test_time):
=1: flexible, ping always runs (min 16s)
=0: strict, test ends after duration
File Structure
run_sl_test.sh # Test engine
run_sl_test_config.sh # Configuration
~/.ssh/config # SSH host aliases
~/openairinterface5g/ # OAI source
<base_dir>/
latest -> test_<ts>/ # Symlink
test_<timestamp>/ # Results
test_summary_*.csv
iperf3_summary_*.csv / *.png
result_*_<test>_<ts>.log
ping_result_*.txt
base_dir priority: -d flag > base_log_dir in config > script directory

## Slide 4
Multi-Host Testing
Test Topologies
Single-Host (Mode 2):
SyncRef UE <--rfsim--> Nearby UE
(both on localhost)
Two-Host (Mode 2):
Local: SyncRef UE (rfsim server)
Remote: Nearby UE (rfsim client)
Three-Host (Mode 1 SRAP):
gNB host: gNB + 5G Core
relay_ue host: Relay UE (Uu + PC5)
remote_ue host: Remote UE (PC5)
Host Assignment per Test Mode
SL Mode | Type | Hosts | gNB | SyncRef UE | Nearby UE
Mode 2 | RFSIM | 1 | — | local | local
Mode 2 | RFSIM | 2 | — | local | remote_ue
Mode 2 | USRP | 2 | — | local | remote_ue
Mode 2 | VRTSIM | 1 | — | local | local
Mode 1 (SRAP) | RFSIM | 1 | local | local | local
Mode 1 (SRAP) | RFSIM | 3 | gNB, local | relay_ue | remote_ue
Mode 1 (SRAP) | USRP | 3 | local | relay_ue | remote_ue
Mode 1 (SRAP) | VRTSIM | 1 | local | local | local
Uu | RFSIM | 1 | local | — | local (nrUE)
Uu | RFSIM | 2 | local | — | nr_ue (nrUE)
Uu | USRP | 2 | local | — | nr_ue (nrUE)
Uu | VRTSIM | 1 | local | — | local (nrUE)
SSH aliases defined in ~/.ssh/config
Passwordless SSH required: ssh-copy-id <alias>

## Slide 5
Test Selection & Configuration
Test Profiles
Profile | Repeats | MCS | Duration | SNR/Atten | Gain | LDPC Iter | Use Case
pilot | 1 | 1 | 30s | 0 / 20dB | 20/110 | 30 | Quick smoke test
regress | 1 | 1, 9 | 30s | 0 / 20dB | 20/110 | 30 | Regression validation
stress | 3 | 9, 16, 28 | 300s | 0 / 20-60dB | 20/110 | 30 | Long-term stability
bler | 12 | 0-28 | 85s | Noise sweep | N/A | 30 | BLER waterfall curves
Per-Profile Test Lists
• pilot_tests / regress_tests / stress_tests
• slmode2_basic_tests — entire group
• slmode2_basic_tests[0:2] — range (indices 0-2)
• slmode2_basic_tests[0] — single test
• test_name:csi:psfch — parametric combo
Additional Config Settings
# Log output directory (default: script dir)
base_log_dir="~/openairinterface5g"
# Use external clock source for USRP (0=internal, 1=external)
use_external_clock=1
# Use standalone mode (0=disabled, 1=enabled)
use_sa=0
# Use gnome-terminal (0=bash, 1=gnome)
use_gnome=1
# Ensure ping test time (0=strict, 1=flexible)
ensure_ping_test_time=1
# USRP serial numbers (SL Mode 1 relay only)
RELAY_UE_USRP_SN_FOR_UU=340EA03
RELAY_UE_USRP_SN_FOR_SL=340EA3B
Running Tests
# use config settings (or defaults)
./run_sl_test.sh
# override log dir and gnome terminal
./run_sl_test.sh -d ~/openairinterface5g
./run_sl_test.sh -g 1
./run_sl_test.sh -d ~/openairinterface5g -g 1
Priority: CLI flags (-d, -g) > config file > defaults

## Slide 6
Four-Tier Configuration System
Override MCS and duration at four levels: test-specific > slice-specific > group-specific > profile-default
Configuration Examples
# In run_sl_test_config.sh
# Group-level (all tests in group)
group_specific_duration["slmode2_basic_tests"]=30
group_specific_mcs["slmode2_basic_tests"]="16,28"
# Slice-level (specific indices)
# [0:2] range, [0,2] pick-list, [2] single
group_specific_duration["slmode2_basic_tests[2]"]=60
group_specific_mcs["slmode2_basic_tests[2]"]="12,16,20,24,28"
# Test-specific (individual test)
test_specific_duration["usrp_B210_pc5_ping_test"]=90
test_specific_mcs["usrp_B210_pc5_ping_test"]="20,24,28"
Key Features
MCS formats: Comma "16,28", space "16 28", or seq "$(seq 0 1 10)"
Auto-discovery: Groups ending with _basic_tests, _iperf3_tests, _csi_psfch_tests
Excluded: pilot_tests, regress_tests, stress_tests (profile arrays)
Priority order:
1. Test-specific → 2. Slice-specific → 3. Group-specific → 4. Profile-default

## Slide 7
Predefined Test Groups
Group | Idx | Test Case
uu_basic_tests | 0 | rfsim_uu_ping_test_on_local_host
 | 1 | vrtsim_uu_ping_test_on_local_host
 | 2 | rfsim_uu_ping_test_on_two_hosts
 | 3 | usrp_B210_uu_ping_test_on_two_hosts
slmode2_basic_tests | 0 | rfsim_pc5_ping_test_on_local_host
 | 1 | vrtsim_pc5_ping_test_on_local_host
 | 2 | rfsim_pc5_ping_test_on_two_hosts
 | 3 | usrp_B210_pc5_ping_test_on_two_hosts
slmode2_csi_psfch_tests | 0 | rfsim_pc5_csi_acquisition_psfch_period_test_on_local_host
 | 1 | vrtsim_pc5_csi_acquisition_psfch_period_test_on_local_host
 | 2 | rfsim_pc5_csi_acquisition_psfch_period_test_on_two_hosts
 | 3 | usrp_B210_pc5_csi_acquisition_psfch_period_test_on_two_hosts
slmode2_iperf3_tests | 0 | rfsim_pc5_iperf3_test_on_local_host
 | 1 | vrtsim_pc5_iperf3_test_on_local_host
 | 2 | rfsim_pc5_iperf3_test_on_two_hosts
 | 3 | usrp_B210_pc5_iperf3_test_on_two_hosts
slmode1_basic_tests | 0 | rfsim_slmode1_srap_ping_test_on_local_host
 | 1 | vrtsim_slmode1_srap_ping_test_on_local_host
 | 2 | rfsim_slmode1_srap_ping_test_on_three_hosts
 | 3 | usrp_B210_slmode1_srap_ping_test_on_three_hosts
slmode1_iperf3_tests | 0 | rfsim_slmode1_srap_iperf3_test_on_local_host
 | 1 | vrtsim_slmode1_srap_iperf3_test_on_local_host
 | 2 | rfsim_slmode1_srap_iperf3_test_on_three_hosts
 | 3 | usrp_B210_slmode1_srap_iperf3_test_on_three_hosts
slmode1_csi_psfch_tests | 0 | rfsim_slmode1_srap_csi_acquisition_psfch_period_test_on_local_host
 | 1 | vrtsim_slmode1_srap_csi_acquisition_psfch_period_test_on_local_host
 | 2 | rfsim_slmode1_srap_csi_acquisition_psfch_period_test_on_three_hosts
 | 3 | usrp_B210_slmode1_srap_csi_acquisition_psfch_period_test_on_three_hosts
Custom Groups
regress_tests=(
slmode2_basic_tests
slmode2_csi_psfch_tests
)
CSI/PSFCH Parameter Format
• test_name — all 8 combos (CSI: 0,1 x PSFCH: 0,1,2,3)
• test_name:0:1 — CSI=0, PSFCH=1 only
• test_name:1: — CSI=1, all PSFCH values
• test_name::2 — PSFCH=2, all CSI values
CSI: sl_CSI_Acquisition (0=enabled, 1=disabled)
PSFCH: sl_PSFCH_Period (0, 1, 2, 3)
Groups resolve recursively — a group can contain other group names

## Slide 8
Available Test Cases
Test Case | Mode | Hosts | Description
rfsim_uu_ping_test_on_local_host | Uu | 1 | gNB <-> UE ping on localhost (requires 5G Core)
rfsim_uu_ping_test_on_two_hosts | Uu | 2 | gNB <-> UE ping across two machines (requires 5G Core)
rfsim_pc5_ping_test_on_local_host | SL Mode 2 | 1 | Basic PC5 ping: SyncRef <-> Nearby UE
rfsim_pc5_ping_test_on_two_hosts | SL Mode 2 | 2 | PC5 ping across two machines
rfsim_pc5_csi_acquisition_psfch_* | SL Mode 2 | 1-2 | CSI/PSFCH parametric sweep (up to 8 combos)
rfsim_pc5_iperf3_test_on_* | SL Mode 2 | 1-2 | iperf3 bandwidth sweep over PC5
rfsim_slmode1_srap_ping_* | SL Mode 1 | 1, 3 | U2N relay ping via SRAP
rfsim_slmode1_srap_iperf3_* | SL Mode 1 | 1, 3 | U2N relay iperf3 bandwidth sweep
rfsim_slmode1_srap_csi_acquisition_psfch_* | SL Mode 1 | 1, 3 | U2N relay CSI/PSFCH parametric sweep (up to 8 combos)
usrp_B210_* | All | 2-3 | USRP hardware variants of above tests
vrtsim_uu_ping_test_on_local_host | Uu | 1 | gNB <-> UE ping over shared-memory radio
vrtsim_pc5_ping_test_on_local_host | SL Mode 2 | 1 | PC5 ping over shared-memory radio
vrtsim_pc5_csi_acquisition_psfch_* | SL Mode 2 | 1 | PC5 CSI/PSFCH parametric sweep over shared-memory radio (8 combos)
vrtsim_pc5_iperf3_test_on_local_host | SL Mode 2 | 1 | PC5 iperf3 bandwidth sweep over shared-memory radio
vrtsim_slmode1_srap_ping_test_on_local_host | SL Mode 1 | 1 | U2N relay ping (SRAP) over shared-memory radio; launch-order/timing sensitive
vrtsim_slmode1_srap_csi_acquisition_psfch_* | SL Mode 1 | 1 | U2N relay CSI/PSFCH parametric sweep over shared-memory radio (8 combos)
vrtsim_slmode1_srap_iperf3_test_on_local_host | SL Mode 1 | 1 | U2N relay iperf3 sweep over shared-memory radio; client binds oaitun_ue2
Pass criteria: >= 60% ICMP ping success rate | PSSCH stats: TX/RX counters extracted from UE logs for each direction

## Slide 9
Test Results & PSSCH Statistics
Summary Table Output
Test Name | Itrn | Hosts | MCS | Runtime | Ping | PSSCH Rate1 | PSSCH Rate2 | Total | Result
==========================================================================================================================================
rfsim_pc5_ping_test_on_local_host | 1 | 1 | 9 | 40s | 100% | 33/33 (100%) | 33/33 (100%) | 100% | PASS
rfsim_pc5_csi_psfch_*_csi0_psfch1 | 1 | 2 | 9 | 44s | 100% | 12/12 (100%) | 8/8 (100%) | 100% | PASS
rfsim_slmode1_srap_ping_test_on_local_host | 1 | 1 | 9 | 58s | 100% | 36/36 (100%) | 38/38 (100%) | 100% | PASS
PSSCH Rate Calculation
Rate1: SyncRef TX -> Nearby RX (RX_nearby / TX_syncref)
Rate2: Nearby TX -> SyncRef RX (RX_syncref / TX_nearby)
Total: Aggregated both directions (RX_sync + RX_nearby) / (TX_sync + TX_nearby)
Log Files (per test)
• test_summary_*.csv — summary table
• iperf3_summary_*.csv / *.png — iperf3 bandwidth/loss plot
• result_<component>_<test_name>_<ts>.log — softmodem output
• ping_result_*.txt — ping output
• iperf3_server_*.txt / iperf3_client_*.txt — iperf3 logs
Remote logs captured via tee, then moved to log folder.
Log file list defined in softmodem_log_files in config.

## Slide 10
Extending the Framework
1. Define Test Function
my_custom_test() {
echo "==== Testing ${FUNCNAME[0]} ===="
[[ $# -ge 1 ]] && duration=$1
[[ $# -ge 2 ]] && test_type=$2
[[ $# -ge 3 ]] && mcs=$3
[[ $# -ge 4 ]] && iteration=$4
local start_time=$(date +%s) sl_mode=2
run_syncref_cmd $test_type $mcs $sl_mode "local"
run_nearby_cmd $test_type $mcs $sl_mode "local"
sleep 5
evaluate_ping_test "local" "oaitun_ue1" \
"10.0.0.100" $sl_mode "${FUNCNAME[0]}"
local end_time=$(date +%s)
print_runtime $start_time $end_time
print_test_summary "${FUNCNAME[0]}" \
"$iteration" "1" "$mcs" ...
}
2. Add rfsim/usrp Wrappers
rfsim_my_custom_test_on_local_host() {
local test_type="rfsim"
my_custom_test $duration $test_type $mcs $iteration
}
usrp_B210_my_custom_test_on_local_host() {
local test_type="usrp"
my_custom_test $duration $test_type $mcs $iteration
}
3. Enable in Config
enabled_tests=(
rfsim_my_custom_test_on_local_host
)
4. Custom Profiles
custom_tests=( slmode2_basic_tests )
elif [[ $test_profile == "custom" ]]; then
enabled_tests=("${custom_tests[@]}")
num_repeat=2; mcs_array=(1 5 9)
duration=60; max_ldpc_iterations=30
atten_array=(20 30 40)

## Slide 11
Troubleshooting & References
Common Issues
Problem | Solution
"No such device" for oaitun_ue1 | UE not initialized — increase sleep after launch
Ping fails (<60%) | Check ip addr show oaitun_ue1; increase duration
PSSCH stats show 0/0 or N/A | Check sidelink logs; verify remote logs copied
SSH command fails | ssh remote_ue hostname — verify passwordless auth
Remote UE config not updated | Check REMOTE_USER var; verify paths on remote
SRAP relay test fails | docker ps ¦ grep oai-amf — verify 5G Core
USRP attenuator error | curl http://169.254.10.10/ — check reachability
Config changes don't persist | Script restores defaults before each test
Prerequisites
• nr-uesoftmodem, nr-softmodem, nr-cuup
• gnome-terminal for parallel process launch
• Docker-based OAI 5G Core (SRAP/Uu tests)
• USRP B210 + RF attenuator (hardware tests)
• Passwordless SSH to all remote hosts
References
Sidelink docs: ~/openairinterface5g/doc/episys/README_SL.md
Config files: ~/openairinterface5g/targets/.../NR-SIDELINK/CONF/
3GPP specs: TS 38.331, TS 38.321, TS 38.211
RF simulator: ~/openairinterface5g/radio/rfsimulator/
License: OAI Public License V1.1